FACT SHEET ON EXPANSION OF SINGAPORE EXPO HALLS

TIMELINE ON DEVELOPMENT OF HALLS 7 - 10

| 2003 | Expansion of Singapore Expo mooted |
| --- | --- |
| March 2004 | Design Architect appointed |
| October 2004 | Physical construction of the halls |
| August 2005 | Temporary Occupation Permit obtained; management of the halls is undertaken by Singex Venues Pte Ltd, the appointed management company for Singapore Expo. |

PROJECT TEAM

| Client | Singapore Tourism Board |
| --- | --- |
| Master Planner / Design Architect | Cox Architects & Planners |
| Project Architect | Liu & Wo Architects Pte Ltd |
| Structural Engineer | Arup Singapore Pte Ltd |
| Electrical & Mechanical Engineer | Lincolne Scott Ng Consulting Engineers |
| Quantity Surveyor | KPK Quantity Surveyors |
| Main Contractor | Kajima Overseas Asia Pte Ltd |

GENERAL SPECIFICATIONS

| Items | Provision |
| --- | --- |
| Construction Period | Oct 2004 to Aug 2005 |
| Site Area | 93,938 sq m |
| Area | 9,936 sq m of columnless space measuring 144m (L) x 69m (W) in each hall |
| Ceiling Height | 8m - 10m at bottom of trusses 11.5m - 13.5m in between |
| Floor Loading | 20 kN/sqm or 20kPa or 417lb/sq ft |
| Ventilation | Central Air-conditioning System at 23 deg C. |
| Hall connectivity | 4 openings between each hall measuring 8.3m (W) x 6m (H) |
| Entrance & Exits | Halls 7 & 10 At front of halls, there are 9 double leaf doors and 4 single leaf doors; At rear of halls, there are 6 double leaf doors only. At the side, there are 16 double leaf doors Hall 8 & 9 At front of halls, there are 9 double leaf doors and 4 single leaf doors; At rear of halls, there are 6 double leaf doors only. |
| Freight Doors | 2 per hall, each measuring 7.5m (W) x 7m (H) |
| Suspension Points | 105 points per hall; 1 tonne (1000kg) per point |
| Electrical Loading | 0.50 MVA per hall (excluding ACMV load) |
| Communications | 4 DPRs not DB (2 front & 2 rear). No outgoing cablings. Fibre Optic from New FCC Room to existing client MDF Room at Hall 6. Connection by others. |
| Service Trenches | Conduits and Electrical Sump pits system. Total 32 sump pits branch out from central concrete trench of 150mm (W) x 200mm (D) by 2 110mm dia. conduit. |
| Water points/ Sewer points | Total 8 water point c/w water meters and 8 floor traps. Both enclosed in a single sump pit (Total 8 per hall) |
| Covered Linkway | Height range from approx 4m clear (at entry canopy) to approx 5.5m high (over Expo Drive to approx. 6.5m high over the taxi lay-by at Foyer 2 of Hall 6. Width of linkway is 5m between columns with 1.5m overhang at sides. |